## Slide 1: GPU Computing
Rohan Saxena, FMG Portfolio Modeling Analytics
12th April 2018

## Slide 2: OVERVIEW
What is GPU
GPU vs CPU
CUDA – CPU+GPU
PROCESS FLOW OF CUDA PROGRAM
SUPPORT TO GPU’s
APPLICATIONS
SPEEDUP
DOWNSIDE

## Slide 3: GPU
•The Graphic Processing Unit (GPU) is a processor that was specialized for processing graphics. Earlier used more in the gaming industry.
•The GPU has recently evolved towards a more flexible architecture.
•OPPORTUNITY: We can implement *any algorithm*, not only graphics.
•CHALLENGE: obtain efficiency and high performance.

## Slide 4: GROWTH IN GPU COMPUTING

## Slide 5: GPU vs CPU
  A CPU consists of a few cores optimized for sequential serial processing
  A GPU consists of thousands of smaller cores designed for parallel processing

## Slide 6: CPU vs GPU
GPU is more aimed towards data processing

## Slide 7: CUDA: Heterogeneous Parallel Computing
CPU optimized for fast single-thread execution
Cores designed to execute 1 thread or 2 threads concurrently
Large caches attempt to hide DRAM access times
Cores optimized for low latency cache access
Complex control logic for speculation and out of order execution
GPU optimized for high multi thread output
Cores designed to execute many parallel threads concurrently
Cores optimized for data-parallel, throughput computation
Chips use extensive multithreading to tolerate DRAM access times
+

## Slide 8: GPU’s with CPU
Few cores in CPU
v/s
1000s of cores in GPU
New Code Structure

## Slide 9: Anatomy of CUDA C Program
Serial code executes in a Host(CPU) thread
Parallel code executes in many concurrent device (GPU) threads across multiple parallel processing elements

## Slide 10: PROCESS FLOW
1. COPY DATA FROM CPU TO GPU
2. LAUNCH KERNEL
3. EXECUTE KERNEL COMMANDS
4. COPY BACK DATA TO CPU

## Slide 11: CUDA THREAD ORGANIZATION
Threads are grouped into blocks
Blocks are grouped into a grid
A Kernel is executed as a grid of blocks of threads

## Slide 12: THREAD HIERARCHY
•Kernels are executed by thread.
•A kernel is a simple C program.
•Each thread has it own ID
•Thousands of threads execute same kernel. (Parallel Computation)
•Threads in a block can synchronize execution
•Blocks are independent (Must be able to be executed in any order, Parallel or Sequential)

## Slide 13: IDENTIFYING EXECUTION FLOW

## Slide 14: SIMPLE NUMBERS TO SHOW SPEEDUP
A simple addition program
__global__ void add(int n, float *x, float *y)
{ int index = blockIdx.x * blockDim.x + threadIdx.x;
int stride = blockDim.x * gridDim.x;
for (int i = index; i < n; i += stride)
y[i] = x[i] + y[i];
}

## Slide 15: SUPPORT
New GPU generation every ~18 months.
•Strong support to GPU computing:
•Hardware side: developing flexible GPUs.
•Software side: releasing and improving development tools.
•Community side: support to academics.

## Slide 16: APPLICATIONS
FMG analytics has a huge scope to integrate out process with GPU’s to scale our applications to the next level
Some Areas:
          COMPUTING
          SIMULATIONS
          MODELLING

## Slide 17: COMPUTATION : AVAR
VARIANCE – COVARIANCE METHOD

## Slide 18: SIMULATIONS
OPTION PRICING:
-Simulating a price of stock assuming Normal Distribution
-Price calculated from expected pay-off
VERY SIMILAR USE-CASE : MonteCarlo VAR in Portfolio Risk Analytics

## Slide 19: MODELLING
REGRESSION
-Speedup is marginal in case of small data, speedup visible when data being utilised is in Millions
MACHINE LEARNING/DEEP LEARNING
-GPU Architecture supports large data
computations very well
-NVIDIA CuDNN is a leader in Deep Learning

## Slide 20: SPEEDUP
•You can get hundred-fold speedup for some algorithms
•It depends on the non-parallel part:
Amdahl’s law.
•Complex application normally make use of many algorithms.
•Look for alternative ways to perform the computations that are more parallel.
•Significance: An accelerated program is going to be as fast as its serial part!

## Slide 21: THE DOWNSIDE
  GPU can’t speed up everything
    E.g. Process involving complex calculations
  Alternatives exist
    Batch/overnight process for time consuming but time insensitive tasks
  Estimated costs of GPU
    Hardware cost: ~$100K for 4 boxes
COST VS USE-CASE?

## Slide 22: Additional Information
CUDA Resources:
For access to FMG owned Compute Engine: David Li, Patrick Guo